## Slide 1: Replica: A Wireless Manycore for Communication-Intensive and Approximate Data
Vimuth Fernando1, Antonio Franques1, Sergi Abadal2,
Sasa Misailovic1, Josep Torrellas1
1University of Illinois at Urbana-Champaign
2 Universitat Politècnica de Catalunya
CCF-1629431
CCF-1703637

## Slide 2
Master Thread​
counter++;
barrier_wait(b)
Worker Threads
barrier_wait(b)
x = counter;
Computations with broadcast and fine-grained data sharing do not scale well in shared-memory multiprocessor architectures
Motivation
Notes: Computations with broadcast and fine-grained data sharing do not scale well in shared-memory multiprocessor architectures
Consider the example program here. A master thread is updating a count that is read by a set of worker threads.

## Slide 3
Manycore with a Network on Chip
Master Thread​
counter++;
barrier_wait(b)
Worker Threads
barrier_wait(b)
x = counter;
Notes: Highlight the lines (hops)
When we run this program on a manycore with a network on chip, where the master thread running on one core while the workers run on the other cores, data sharing and synchronization happens through sending messages using the wired network on chip.
As chip sizes grow, the amount of messages that occur due to such broadcast data sharing can lead to communication bottlenecks, and significant delays to go through the cache hierarchy.
----------------------------------------------------
the state of the art is wired network-on-chip, which connects all cores""however since it cannot have all to all connections and couple with cache hierarchies there are significant delays when transferring data from one core to all the remaining cores

## Slide 4: WiSync: On-chip Wireless Communication for Synchronization
Abadal et al. "WiSync: an architecture for fast synchronization through on-chip wireless communication." ASPLOS 2016
Core
Broadcast memory
(16 KB)
Notes: Couple of years ago WE PRESENTED
Wisync a recently proposed architecture looked at using wireless communication on a chip to handle synchronization
Wisync augments the existing wired network on the chip with a wireless network used to broadcast messages
The data being communicated using the wireless network resides in a dedicated segment of memory called the broadcast memory

## Slide 5: WiSync: On-chip Wireless Communication for Synchronization
Wireless Antenna and Transceiver
Broadcast memory
(replicated contents)
Abadal et al. "WiSync: an architecture for fast synchronization through on-chip wireless communication." ASPLOS 2016
Notes: Per core / same data. We call it replicated memory
In wysinc all cores on a manycore chip has its own wireless antenna and a transceiver along with a broadcast memory
All of these memories contain the same data and any update is broadcasted across the chip in 5 cycles

## Slide 6: WiSync: On-chip Wireless Communication for Synchronization
Core3
…
b
…
Core15
…
b
…
Master Thread​
barrier_wait(b)
Core0
…
b
…
Notes: “In wisync”
The barrier from our example can be allocated in the broadcast memory. And each core will have its own copy
When the master thread arrives at the barrier it can send a broadcast signal across the chip and update all the copies of the barrier at once.
Wisync showed that using wireless for synchronization can significantly speed up applications

## Slide 7: WiSync: On-chip Wireless Communication for Synchronization
Core3
…
b
…
Core15
…
b
…
Master Thread​
barrier_wait(b)
Core0
…
b
…
Notes: The barrier from our example can be allocated in the broadcast memory. And each core will have its own copy
When the master thread arrives at the barrier it can send a broadcast signal across the chip and update all the copies of the barrier at once.
Wisync showed that using wireless for synchronization can significantly speed up applications

## Slide 8: WiSync: On-chip Wireless Communication for Synchronization
Core0
…
b
…
Core3
…
b
…
Core15
…
b
…
Master Thread​
barrier_wait(b)
Notes: The barrier from our example can be allocated in the broadcast memory. And each core will have its own copy
When the master thread arrives at the barrier it can send a broadcast signal across the chip and update all the copies of the barrier at once.
Wisync showed that using wireless for synchronization can significantly speed up applications

## Slide 9
In WiSync, ordinary data uses the wired network
Master Thread​
counter++
Worker Threads
x = counter;
Notes: In wisync
But ordinary data such as the count from our example still is shared using the wired network even if they are shared globally

## Slide 10: Can we leverage wireless communication to speed-up transfers of ordinary shared data?
Key Question
Notes: So, The key question we looked at in this paper is Can we use wireless communication to speed-up transfers of ordinary communication-intensive data?

## Slide 11: Contributions: Replica
A manycore architecture and software interface for wireless communication (sync and ordinary data)
Hardware innovations
  Adaptive wireless protocol
  Selective packet dropping
Software innovations
  Transformations and tools to adapt applications to wireless
  Optimizations for approximate computing
For 64 core execution: speedup applications by 1.89x over a conventional multicore
Notes: Our paper present Replica, A manycore architecture and software interface for wireless communication
Replica presents several hardware innovations
In the form of an Adaptive wireless protocol and a Selective packet dropping mechanism
Along with several software innovations such as Transformations and tools to adapt applications to wireless communication and
  Optimizations for approximate computing
For 64 core executions Replica can speedup applications by 1.89x over a conventional multicore

## Slide 12: Replica Architecture
Core
Controller
L1 Cache
Transceiver
L2 Cache
BMem
Antenna
Wired
network
Directory
32-512 KB
Notes: Similar to wisync we augment the existing wired network and cache hierarchy with the wireless network and broadcast memory
We use a broadcast memory of up to 512 KB
This is memory mapped. The memory controller redirects memory accesses to either the Bmem or regular cache hierarchy based on the address being accessed

## Slide 13: Example
int* A = (int*) wireless_malloc(size)
​int* B = (int*) malloc(size)
BMem
A
B
Regular Memory
Notes: A developer can change the allocation sites of data structures to be allocated in the broadcast memory
And our library allocates them in the BMem
--- TODo
“Only” malloc
No other change necessary

## Slide 14
Core
Controller
L1 Cache
Transceiver
L2 Cache
BMem
Antenna
Wired
network
Directory
Write
Notes: When a thread running on a core writes to a data structure in the bmem replica sends a wireless message

## Slide 15
Core
Controller
L1 Cache
Transceiver
L2 Cache
BMem
Antenna
Wired
network
Directory
Atomic update of local and all remote BMems
Write
Notes: If the message is successfully sent, the local Bmem and all remote bmems are updated togethre

## Slide 16
Broadcast Memory for ordinary data
Core0
…
counter:0
…
Core3
…
counter:0
…
Core15
…
counter:0
…
Master Thread​
counter++;
Notes: We can use the broadcast memory to hold the count and when the master thread updates it we can broadcast the change to all the copies held in the other broadcast memories

## Slide 17
Broadcast Memory for ordinary data
Core0
…
counter:1
…
Core3
…
counter:1
…
Core15
…
counter:1
…
Master Thread​
counter++;
Notes: We can use the broadcast memory to hold the count and when the master thread updates it we can broadcast the change to all the copies held in the other broadcast memories

## Slide 18
Replica: Wireless channel
One channel shared by all the cores
Everyone receives what one core transmits
Only one core can transmit at a given time
  ensures the same order of updates across all BMems
Notes: Replica has one wireless channel shared by all the cores
Everyone receives what someone transmits
Only one core can transmit at the same time
  Replica ensures a same order of updates across all bmem

## Slide 19
Core
Controller
L1 Cache
Transceiver
L2 Cache
BMem
Antenna
Wired
network
Directory
Reads
Read: Local access
Notes: Reads are satisfied using the local bmem

## Slide 20: Challenges
Limited wireless bandwidth: Only one core can transmit at a time
Bounded size of the BMem: Arbitrary data structures will not fit
Notes: Using wireless communication for ordinary data presents two fundamental challenges
Limited wireless bandwidth: Only one core can communicate at a time
Bounded size of the BMem: Arbitrary data structures will not fit

## Slide 21: Solutions
Limited wireless bandwidth: Only one core can transmit at a time
  Adaptive wireless protocol
  Selective message dropping
  Approximate transformations to use less bandwidth
Bounded size of the BMem: Arbitrary data structures will not fit
Notes: Animate
Replica is geared to handle this two challenges

## Slide 22: Solutions
Limited wireless bandwidth: Only one core can transmit at a time
  Adaptive wireless protocol
  Selective message dropping
  Approximate transformations to use less bandwidth
Bounded size of the BMem: Arbitrary data structures will not fit
  Software transformations to fit most important structures in BMem
  Approximate transformations to use BMem effectively
  Tools to identify/autotune highly-shared data structures
Notes: Animate
Replica is geared to handle this two challenges

## Slide 23
Wireless protocol organizes the accesses to the wireless network
Two wireless protocols can be used based on application behavior
  Broadcast Reliability Sensing protocol (BRS)
  Token Ring protocol
Wireless Protocol
Notes: Wireless protocol ensures that only one core communicates at a time
Two wireless protocols can be used based on application behavior
  BRS protocol
  Token ring protocol

## Slide 24
Wireless Message
4 cycles at 20Gb/s*
Time
0
1
2
3
4
5
Address
Value
C
* Yu, et al. “Architecture and Design of Mul5-Channel Millimeter-Wave Wireless Network-on-Chip,” IEEE Design & Test, 2014 (scaled)
Notes: In replica a message in the wireless network consist of the address, the value being written to that address and several control bits
At the wireless speed of 20gb/s transmitting this message would take 5 cycles
Yu, et al. “Architecture and Design of Mul5-Channel Millimeter-Wave Wireless Network-on-Chip,” IEEE Design & Test, 2014 (scaled)

## Slide 25
Start sending message if the medium is free
Two cores starting at the same time results in a collision
Broadcast Reliability Sensing Protocol (BRS)
Notes: This protocol has no wasted cycles in high contention but can cause unnecessary delays when only a few cores have messages to transmit

## Slide 26: Broadcast Reliability Sensing Protocol (BRS)
Time
0
1
2
3
4
5
Check if collision occurred
Check if medium is free
Notes: Don’t say preamble ---- First chunk
The Broadcast Reliability Sensing Protocol adds one cycle to this transmission to detect collision
In the BRS protocol, when a core wants to transmit a message it first checks to see if the wireless medium is free.
If it is, the part of the message is transmitted for 1 cycle. the transceiver then listens if there was a collision with another packet in the first cycle.
If not, the rest of the message is transmitted in 4 cycles

## Slide 27: Broadcast Reliability Sensing Protocol (BRS)
Time
Core 0
Core 1
Notes: If two cores try to transmit at once, they will see that a collision occurred in the second cycle when they listen.
Then both cores will backoff for a randomized amount of time and try again
------------------ TIDO
How do they know

## Slide 28: Broadcast Reliability Sensing Protocol (BRS)
Time
No wasted cycles if low contention
Lot of collisions if high contention
Core 0
Core 1
Notes: This will keep happening until the message is sent.
This protocol has no wasted cycles if the contention is low. But in high contention situations the number of collisions increase and latencies grow.

## Slide 29: Token Ring Protocol
Pass conceptual token among cores
Can send wireless message only if the core owns the token
Notes: This protocol has no wasted cycles in high contention but can cause unnecessary delays when only a few cores have messages to transmit

## Slide 30: Token Ring Protocol
Core 0
Core 1
Time
Core 2
Core 3
No wasted cycles if high contention
Unnecessary delays if low contention
Notes: Explain this more
In a token ring based protocol all cores wait for their turn in the form of a logical token being passed around.
A core can only start transmitting if it owns the token

## Slide 31
In Replica, the utilization of the wireless network vary across applications and within an application
  Sparse traffic – BRS
  Bursty traffic – Token Ring
Replica uses an adaptive dynamic protocol that switches between the two by observing communication behavior
  Number of collisions
  Number of skipped token slots
Adaptive Wireless Protocol
Notes: Replica uses an adaptive dynamic protocol that switches between the two protocols based on the observed traffic in the system

## Slide 32: Approximate transformations to use less bandwidth
Every write to data in the BMem results in a message being broadcasted
We can reduce the pressure on the network by skipping some of the writes
  Reducing communication at the cost of accuracy
Many programs have shared data structures that are amenable to approximations
Notes: We can further reduce contention on the network using approximate methods.
Every write to data in the BMem results in a message being broadcasted
We can reduce the pressure on the network by skipping some of the writes.
While this can introduce some errors into the program, Many programs have shared data structures that are amenable to such approximations.

## Slide 33: Opportunity in Replica: Dropping Messages
All cores see the contention in the wireless network
Can drop messages while maintaining the same state across all cores
Notes: In a consistent manner. Why?
Replica provides a great opportunity to implement this approximation in hardware
All cores see the contention in the wireless network
Can drop messages while maintaining the same state across all cores

## Slide 34: Approximate stores
Developers indicate approximable data structures
  approx_wireless_malloc(size)
Stores to approximable variables are dropped if they cannot access the wireless network before a given threshold
Notes: we keep track of the time each message speds in the buffer before being sent. When that threshold is exceeded we remove that message from the buffer.
This reduces the contention on the network and therfore reduces the latency of remaining packets
--- TODO
Memory mapped
No other changes needed

## Slide 35: Approximate stores
Developers indicate approximable data structures
  approx_wireless_malloc(size)
Stores to approximable variables are dropped if they cannot access the wireless network before a given threshold
Notes: we keep track of the time each message speds in the buffer before being sent. When that threshold is exceeded we remove that message from the buffer.
This reduces the contention on the network and therfore reduces the latency of remaining packets
--- TODO
Memory mapped
No other changes needed

## Slide 36: Approximate transformations to use less bandwidth
We used the approximate stores to implement primitives such as Approximate Locks
  Spin lock that gives up trying to acquire a lock after some time
Existing approximate techniques that reduce communication more useful in this resource constrained setting
  Example: Skipping negligible updates to shared data
Notes: We can further reduce contention on the network using approximate methods.
Every write to data in the BMem results in a message being broadcasted
We can reduce the pressure on the network by skipping some of the writes.
While this can introduce some errors into the program, Many programs have shared data structures that are amenable to such approximations.

## Slide 37: Addressing Bounded size of the BMem
Software transformations to fit most important structures in BMem
Approximate transformations to use BMem effectively
  Example: Numerical precision reduction, Cyclic collection update
Tools to identify highly-shared data and tune the application
See the paper for more details
Notes: In addition to the wireless medium, the bounded size of the broadcast memory also present a challenge.
We introduce several software transformations that can be used to fit only most important data structures that require broadcast communication in the BMem
In addition we looked at Approximate transformations such as Numerical precision reduction that can be used to reduce the memory footprint of data structures to fit them into the bmem
We aslo developed tools such as profilers to identify highly-shared data and autotuners to tune the application

## Slide 38: Evaluation
Cycle-level architectural simulations using Multi2sim
  64 core chip
  32-512 KB BMem
  2D Mesh wired network
Applications
  10 benchmarks from PARSEC and CRONO
  Multiple domain: Scientific simulations, computer vision, and graph applications
Notes: Broadcast, many-to-many,

## Slide 39: Benchmarks: Communication Patterns
Benchmark | Sharing Pattern | 
Water | Broadcast | 
BFS | Irregular: many-to-many | 
Bodytrack | One-to-many | 
SSSP | Irregular: many-to-many | 
Canneal | Irregular | 
CC | Irregular: many-to-many | 
Streamcluster | One-to-many, reduction | 
Pagerank | Irregular: many-to-many | 
Community | Irregular: many-to-many | 
Volrend | One-to-many | 

## Slide 40
Chart: 
| Water | BFS | BTrack | SSSP | Canneal | CC | SCluster | Pagerank | Comm | Volrend | GeoMean
Series 1 | 0.98 | 1.43 | 1.01 | 1.64 | 1.03 | 1.59 | 7.2 | 1.16 | 1.02 | 0.91 | 1.4026
Series 2
Series 3
Speedup
BMem for sync variables (WiSync)
1.4x speed up over conventional wired multicore (Geometric Mean)
7.2
1.4x

## Slide 41
Chart: 
| Water | BFS | BTrack | SSSP | Canneal | CC | SCluster | Pagerank | Comm | Volrend | GeoMean
Series 1 | 0.98 | 1.43 | 1.01 | 1.64 | 1.03 | 1.59 | 7.2 | 1.16 | 1.02 | 0.91 | 1.4026
Series 2 | 0.25 | 1.72 | 0.21 | 0.15 | 0 | 0.39 | 2.57 | 0.252 | 0.14 | 0.11 | 0.35519
Series 3
Speedup
BMem for shared data
7.2 -> 9.77
1.4x
1.76x
1.76x speed up (Geometric Mean)

## Slide 42: Benchmarks: Approximation
Benchmark | Sharing Pattern | Approximations
Water | Broadcast | Precision reduction and Approximate Locks
BFS | Irregular: many-to-many | Approximate Stores
Bodytrack | One-to-many | Approximate Stores
SSSP | Irregular: many-to-many | Approximate Stores
Canneal | Irregular | Approximate Locks
CC | Irregular: many-to-many | Approximate Stores
Streamcluster | One-to-many, reduction | Cyclic collection updates
Pagerank | Irregular: many-to-many | Skipping negligible updates
Community | Irregular: many-to-many | Approximate Stores
Volrend | One-to-many | Approximate Stores

## Slide 43
Chart: 
| Water | BFS | BTrack | SSSP | Canneal | CC | SCluster | Pagerank | Comm | Volrend | GeoMean
Series 1 | 0.98 | 1.43 | 1.01 | 1.64 | 1.03 | 1.59 | 7.2 | 1.16 | 1.02 | 0.91 | 1.4026
Series 2 | 0.25 | 1.72 | 0.21 | 0.15 | 0 | 0.39 | 2.57 | 0.252 | 0.14 | 0.11 | 0.35519
Series 3 | 0.27 | 0.13 | 0.03 | 0.04 | 0.01 | 0.19 | 0 | 0.188 | 0.23 | 0.12 | 0.1471
Speedup
BMem for shared data + approximations
On average 1.89x speed up
7.2 -> 9.77
1.4x
1.76x
1.89x
Notes: Same transformations in a conventional wired multicore: 1.04x

## Slide 44
Chart: 
| Water | BFS | Btrack | SSSP | Canneal | CC | SCluster | Pagerank | Comm | Volrend | GeoMean
Series 1 | 0.775 | 0.42 | 0.87 | 0.66 | 0.79 | 0.55 | 0.12 | 0.65 | 0.79 | 0.96 | 0.58635
Energy and area
Energy consumption
Since faster execution: 33% energy reduction
Replica components: 9% of total energy consumed

## Slide 45
Energy and area
15% increase in the area
  11% from the BMem + 4% from the transceiver/antenna
  Using the same area to increase the L2 cache has little impact on performance (1.04x speedup)
Since faster execution: 33% energy reduction
Replica components: 9% of total energy consumed
Chart: 
| Water | BFS | Btrack | SSSP | Canneal | CC | SCluster | Pagerank | Comm | Volrend | GeoMean
Series 1 | 0.775 | 0.42 | 0.87 | 0.66 | 0.79 | 0.55 | 0.12 | 0.65 | 0.79 | 0.96 | 0.58635
Energy consumption

## Slide 46: Also in the paper
Scalability analysis
Power evaluation
Area consumption
Architecture sensitivity analysis
Effectiveness of profiler and autotuner
Statistics on developer effort to adapt programs

## Slide 47: Conclusions
Replica: a manycore that uses a wireless NoC to communicate ordinary data
Hardware and Software innovations
  Adaptive wireless protocol
  Selective packet dropping
  Software techniques to identify and allocate shared data in BMem
  Software transformations for approximate computing
Effectively supports communication-intensive computations
Average speedup of 1.89x over conventional machines
Notes: Animate